# Lab: Advanced Functions
Problems for in-class lab for the "JavaScript Advanced" course @ SoftUni. Submit your solutions in the SoftUni judge system at https://judge.softuni.bg/Contests/2764/Advanced-Functions-Lab.
# Area and Volume Calculator
Write a function which calculates the area and the volume of a figure, which is defined by its coordinates
(x, y, z)
area()
function area() { / return Math.abs(this.x * this.y); / };

vol()
function vol() { / return Math.abs(this.x * this.y * this.z); / };

solve()
function solve(area, vol, input) { / //ToDo.... / }

### Input
You will receive 3 parameters - the functions area and vol and a string, which contains the figures' coordinates.
For more information check the examples.
### Output
The output should be returned as an array of objects. Each object has two properties: the figure's area and volume.
[
  { area: ${area1}, volume: ${volume1} },
  { area: ${area2}, volume: ${volume2} },
  . . .
]
### Note:
Submit only the solve function.
### Examples
Sample Input	Output
area, vol, '[ / {"x":"1","y":"2","z":"10"}, / {"x":"7","y":"7","z":"10"}, / {"x":"5","y":"2","z":"10"} / ]'	[ / { area: 2, volume: 20 }, / { area: 49, volume: 490 }, / { area: 10, volume: 100 } / ]
area, vol, '[ / {"x":"10","y":"-22","z":"10"}, / {"x":"47","y":"7","z":"-5"}, / {"x":"55","y":"8","z":"0"}, / {"x":"100","y":"100","z":"100"}, / {"x":"55","y":"80","z":"250"} / ]'	[ / { area: 220, volume: 2200 }, / { area: 329, volume: 1645 }, / { area: 440, volume: 0 }, / { area: 10000, volume: 1000000 }, / { area: 4400, volume: 1100000 } / ]

# Add
Write a program that keeps a number inside its context and returns new function that adds a given number to the previous one.
### Input
Check the examples below to see how your code will be executed
### Output
Your function should return the final result .
### Examples
Sample Input	Output
let add5 = solution(5); / console.log(add5(2)); / console.log(add5(3));	7 / 8
let add7 = solution(7); / console.log(add7(2)); / console.log(add7(3));	9 / 10

# Currency Format
Write a higher-order function createFormatter that fixes some of the parameters of another function. Your program will receive four parameters: three values and a function that takes 4 parameters and returns a formatted string (a monetary value with currency symbol).
Your task is to return a partially applied function, based on the input function, that has its first three parameters fixed and only takes one parameter.
You will receive the following function:
currencyFormatter
function currencyFormatter(separator, symbol, symbolFirst, value) { / let result = Math.trunc(value) + separator; / result += value.toFixed(2).substr(-2,2); / if (symbolFirst) return symbol + ' ' + result; / else return result + ' ' + symbol; / }

Receive and set the following parameters to fixed values:
separator
symbol
symbolFirst
The final parameter value is the one that the returned function must receive.
### Input
You will receive four parameters:
- separator (string)
- symbol (string)
- symbolFirst (Boolean)
- formatter (function)
### Output
You need to return a function that takes one parameter - value
### Examples
Sample Input
let dollarFormatter = createFormatter(',', '$', true, currencyFormatter); / console.log(dollarFormatter(5345)); // $ 5345,00 / console.log(dollarFormatter(3.1429)); // $ 3,14 / console.log(dollarFormatter(2.709)); // $ 2,71

# Filter Employees
Write a program that filters the employees of your company. You should print the result in a specific format. You will receive 2 parameters (data, criteria). You should parse the input, find all employees that fullfil the citeria and print them.
### Input
You will receive a string with all the employees, and a criteria by witch you should sort the employees. If the criteria is "all" print all the employees in the given format.
### Output
The output should be the printed on the console.
For more information check the examples.
### Examples
Sample Input	Output
`[{ / "id": "1", / "first_name": "Ardine", / "last_name": "Bassam", / "email": "abassam0@cnn.com", / "gender": "Female" / }, { / "id": "2", / "first_name": "Kizzee", / "last_name": "Jost", / "email": "kjost1@forbes.com", / "gender": "Female" / }, / { / "id": "3", / "first_name": "Evanne", / "last_name": "Maldin", / "email": "emaldin2@hostgator.com", / "gender": "Male" / }]`, / 'gender-Female'	0. Ardine Bassam - abassam0@cnn.com / 1. Kizzee Jost - kjost1@forbes.com
`[{ / "id": "1", / "first_name": "Kaylee", / "last_name": "Johnson", / "email": "k0@cnn.com", / "gender": "Female" / }, { / "id": "2", / "first_name": "Kizzee", / "last_name": "Johnson", / "email": "kjost1@forbes.com", / "gender": "Female" / }, { / "id": "3", / "first_name": "Evanne", / "last_name": "Maldin", / "email": "emaldin2@hostgator.com", / "gender": "Male" / }, { / "id": "4", / "first_name": "Evanne", / "last_name": "Johnson", / "email": "ev2@hostgator.com", / "gender": "Male" / }]`, / 'last_name-Johnson'	0. Kaylee Johnson - k0@cnn.com / 1. Kizzee Johnson - kjost1@forbes.com / 2. Evanne Johnson - ev2@hostgator.com

# Command Processor
Write a program that keeps a string inside its context and can execute different commands that modify or print the string on the console.
append(string) - append the given string at the end of the internal string
removeStart(n) - remove the first n characters from the string, n is an integer
removeEnd(n) - remove the last n characters from the string, n is an integer
print - print the stored string on the console
### Input
Check the examples below to see how your code will be executed
### Output
Whenever you receive the command print, the output should be the printed on the console.
### Examples
Sample Input	Output
let firstZeroTest = solution(); / firstZeroTest.append('hello'); / firstZeroTest.append('again'); / firstZeroTest.removeStart(3); / firstZeroTest.removeEnd(4);	loa
let secondZeroTest = solution(); / secondZeroTest.append('123'); / secondZeroTest.append('45'); / secondZeroTest.removeStart(2); / secondZeroTest.removeEnd(1); / secondZeroTest.print();	34

# List Processor
Using a closure, create an inner object to process list commands. The commands supported should be the following:
- add <string> - adds the following string in an inner collection.
- remove <string> - removes all occurrences of the supplied <string> from the inner collection.
- print - prints all elements of the inner collection joined by ",".
### Input
The input will come as an array of strings - each string represents a command to be executed from the command execution engine.
### Output
For every print command - you should print on the console the inner collection joined by ","
### Examples
Input	Output
['add hello', 'add again', 'remove hello', 'add again', 'print']	again,again
['add pesho', 'add george', 'add peter', 'remove peter','print']	pesho, george

# Cars
Write a closure that can create and modify objects. All created objects should be kept and be accessible by name. You should support the following functionality:
- create <name> - creates an object with the supplied <name>
- create <name> inherits <parentName> - creates an object with the given <name>, that inherits from the parent object with the <parentName>
- set <name> <key> <value> - sets the property with key equal to <key> to <value> in the object with the supplied <name>.
- print <name> - prints the object with the supplied <name> in the format "<key1>:<value1>,<key2>:<value2>…" - the printing should also print all inherited properties from parent objects. Inherited properties should come after own properties.
### Input
The input will come as an array of strings - each string represents a command to be executed from your closure.
### Output
For every print command - you should print on the console all properties of the object in the above mentioned format.
### Constraints
All commands will always be valid, there will be no nonexistent or incorrect input.
### Examples
Input	Output
['create c1', / 'create c2 inherit c1', / 'set c1 color red', / 'set c2 model new', / 'print c1', / 'print c2']	color:red / model:new, color:red